## Slide 1
Video Intercom
2021·H1
International Product and Solution Center
Naming Rule

## Slide 2
Main Station |  |  |  |  | 
Main Station | ① | ② | ③ | ④ | ⑤
 | DS-KM | 9 | 5 | 0 | 3
 | Hikvision Video Intercom Main Station Product | 8: Digital product 9: Android product | 3: 7' with touch screen 5: 10.1' with touch screen | Different housing | 1: 0.3 mega pixel resulotion 3: 2 mega pixel resulotion
Example | DS-KM9503 |  |  |  | 
Indoor Station |  |  |  |  |  |  |  |  | 
Indoor Station | ① | ② | ③ | ④ | ⑤ |  | ⑥ | ⑦ | ⑧
 | DS-KH | 8 | 5 | 1 | 1 | — | W | T | E1
 | Hikvision Video Intercom Indoor Station Product | 2: Analog product(4 line) 6: Value product 8: Pro product 9: Ultra product | 0: 3.5' without touch screen 1: 4.3' with touch screen 2: 7' without touch screen 3: 7' with touch screen 5: 10.1' with touch screen | 0/1/2/3: Different housing | 0: without camera 1: 0.3 mega pixel resulotion |  | W: Wi-Fi | T: TF Card | E0: Private Poe E1: Standard Poe E2: 2-Wire E6: Only 12V power supply
Example | DS-KH9510-WTE1 |  |  |  |  |  |  |  | 

## Slide 3
Door Station |  |  |  |  |  |  |  |  | 
Door Station | ① | ② | ③ | ④ | ⑤ |  | ⑥ | ⑦ | ⑧
 | DS-KD | 8 | 0 | 0 | 3 | —— | I | M | E1
 | Hikvision Video Intercom Door Station Product | 3: Value product 8: Pro product 9: Ultra product | 0: 3.5'and below screen with mechanical keypad 1: 3.5' and below screen with touch keypad 2: 4.3' and below screen with touch keypad 6: 10' touch screen | 0/1/2/3: Different housing | 0: without camera 1: 0.3 mega pixel resulotion 2: 1.3 mega pixel resulotion 3: 2 mega pixel resulotion |  | I: Infared Light V: White Light F: fingerprint | M: Mental P: Plastic | E0: Private Poe E1: Standard Poe E2: 2-Wire E6: Only 12V power supply
Example | DS-KD8003-IME1 |  |  |  |  |  |  |  | 
Modular Door Station |  |  |  |  | 
Door Station | ① |  | ② |  | ③
 | DS-KD (8003) | — | KK | — | /surface
 | Hikvision Video Intercom Modular Door Station Product |  | KK：Nametag module KP：Keypad module BK：Blank module M：Mifare card reader module (13.56 MHz) E：EM card reader module (125 kHz) IN：Indicator module DIS：Display module |  | /surface: Surface mounting /flush: Flush mounming /F:flush mouning /S: Stainless /NS: Withour keypad
Example | DS-KD8003-IME1 |  |  |  | 

## Slide 4
Villa Door Station |  |  |  |  |  |  |  |  | 
Villa Door Station | ① | ② | ③ | ④ | ⑤ |  | ⑥ | ⑦ | ⑧
 | DS-KV | 8 | 1 | 1 | 3 | —— | W | M | E1
 | Hikvision Video Intercom Door Station(Villa) Product | 6: Value product 8: Pro product | 1: 1 button 2: 2 button 3: 3 button 4: 4 button | 0/1: Different housing | 0: without camera 1: 0.3 mega pixel resulotion 2: 1.3 mega pixel resulotion 3: 2 mega pixel resulotion |  | I: Infrared Light V: White Light W: Wi-Fi | M: Mental P: Plastic | E0: Private PoE E1: Standard PoE
Example | DS-KV8113-WME1 |  |  |  |  |  |  |  | 
Door Bell (Door Station) |  |  |  |  |  |  |  |  | 
Door Bell (Door Station) | ① | ② | ③ | ④ | ⑤ |  | ⑥ | ⑦ | ⑧
 | DS-KB | 8 | 1 | 1 | 3 | —— | I | M | E1
 | Hikvision Video Intercom Door Station(Door Bell) Product | 6: Value product 8: Utral product | 1: 1 button | 0/1: Different housing | 0: without camera 1: 0.3 mega pixel resulotion 2: 1.3 mega pixel resulotion 3: 2 mega pixel resulotion |  | I: Infared Light V: White Light W: Wi-Fi | M: Mental P: Plastic | E0: Private PoE E1: Standard PoE
Example | DS-KB8113-IME1 |  |  |  |  |  |  |  | 

## Slide 5
Suite |  |  |  |  |  | 
Suite | ① | ② | ③ | ④ |  | ⑤
 | DS-KIS | 2 | 0 | 3 | —— | P
 | Hikvision Video Intercom Suite Product | 1: Analog product(2 wire) 2: Analog product(4 wire) 6: Pro IP product 7: 2-Wire product 9: Ultra IP product | Reserved | 1/2/3/4: Different Conbianition |  | P: with Power
Example | DS-KIS203 |  |  |  |  | 
Power Supply |  |  |  |  | 
Power Supply | ① | ② |  | ③ | ④
 | DS-KAW | 50 | —— | 1 | N
 | Hikvision Video Intercom Door Station Power Supply | 50: Output power 50w |  | 1: 12V 2: 24V | N: Without cabinet
Example | DS-KAW50-1 |  |  |  | 

## Slide 6
Thanks
International Product and Solution Center