## Slide 1
AX PRO Series Product
Online Operation Training
International Product and Solution Center
Notes: 封面
产品图可替换，配图无需更换

## Slide 2
AX PRO System topology
Wireless Panel
Internet
ARC
CCTV system
Mobile phone
SMS/Alarm call/APP
433MHz
Radio Frequency
433MHz
Radio Frequency
Wireless zones
Wireless Outputs
Wireless
Arming Tools
Remote and local programming option
Wired Input
Wired Output

## Slide 3
Keyfob
APP
Villa Solution
IPC
Magnetic Contact
AX PRO Hub
Indoor Sounder
PIR CAM
Panic Button
Break Glass PIR
Keypad
Outdoor Sounder

## Slide 4
Description | Model | Picture
AX PRO Kit | DS-PWA96-Kit-WB | 
Wireless PIR Break-Glass | DS-PDPG12P-EG2-WB | 
Wireless Panic Button | DS-PDEB1-EG2-WB | 
Wireless PIRCAM | DS-PDPC12P-EG2-WB | 
Wireless Keypad | DS-PK1-E-WB | 
Wireless Internal Sounder | DS-PS1-I-WB | 
Wireless External Sounder | DS-PS1-E-WB | 
IPC | Hikvision IP Camera & IPC with Onvif | 
Villa Solution
Internal Use Only

## Slide 5
01
Activing and Connect AX PRO into Network via Wi-Fi/LAN/SIM
Activing
AX PRO
Notes: 分类页

## Slide 6
System Status
Indicators
Power
Supply LED
Built-in Tag Reader
Power Switch
SIM card
Slots (2)
Tamper
Switch
Reset
Button
RS232 Port
Power
Supply
LAN Interface
(RJ45)
Front of AX PRO
Rear of AX PRO
AX PRO Control Panel

## Slide 7
Adding AX PRO into Hik-Connect
Adding via Wi-Fi
(Option 1)
Cloud status indicator
Insert SIM card backboard
Adding via SIM Card
(Option 2)
Adding via LAN
(Option 3)

## Slide 8
Dual buttons for Arming and Disarming
Area Interface
Device List
System Status
AX PRO has a more logical directory in Hik-Connect, which is divided into Area / Device / Status.
Besides, these readable icons also help us know more status of all the system, such as Area Arming Status, RF Signal Strength, battery life, and other system status.

## Slide 9
02
Register wireless detectors and accessories into AX PRO panel
Adding
Peripherals
Notes: 分类页

## Slide 10
1.Adding Keypad
Press ‘+’ to add
Scan QR code of the keypad
Power up keypad and finish
Power Switch
Keypad Setting interface

## Slide 11
2.Setting Keypad Password
Press ‘user’ to
User interface
Turn to
User management site
“Change Keypad Password”
Set a password and press OK

## Slide 12
2.Keypad Operation Video
Adding Keypad
Setting Keypad Password

## Slide 13
3.Adding Keyfob
Press ‘+’ to add
Scan the QR code of Keyfob
Press Arm button to add
Set and finish

## Slide 14
4.Adding Detector (e.g. PIRCAM)
Press ‘+’ to add
Scan the QR code of PIRCAM
Power up PIRCAM and finish
Press Setting Button to configure
PIRCAM Setting interface

## Slide 15
4.Adding Detector Video (e.g. PIRCAM)

## Slide 16
5.Adding Sounder
Press ‘+’ to add
Scan the QR code of Siren
Power up and add
Set and finish

## Slide 17
Adding other AX PRO Series detectors and accessory
Option 1. Scan the QR code on peripheral and then power the device on within 30s, the device will be added when the indicator flashes green for 7 times.
Option 2. we can also turn to “Enrollment Mode”in APP and then register multiple peripherals in group at one time.
In AX PRO system, the enrollment step will show after scanning QR code, and all the peripherals follow this enrollment logic consistently. Saving learning costs efficiently.

## Slide 18
Adding AX PRO Series detectors and accessory
In AX PRO system, we can easily check more kinds of status of peripherals after adding.

## Slide 19
03
Adding RF Repeater.
Auto-pairing features
Repeater
Configuration
Notes: 分类页

## Slide 20
RF Repeater
AX PRO Series RF Repeater
AX PRO Series Repeater is a radio signal ranger extender that can boost the RF communication range for AX PRO wireless alarm system.

## Slide 21
AX PRO
RF Repeater
RF Repeater
RF Repeater
RF Repeater
Normal Detector
Accessory
Sounder
Output
PIRCAM
System Topology

## Slide 22
Strong
Middle
Weak
Offline
AX PRO
Repeater
After added into AX PRO system, the RF Repeater will automatically find and connect the wireless peripherals with weak RF signal, help boost their communication range.
(PIRCAM and Smoke Detector are excepted)
Have to click “Pairing” manually in App or Web to boost the range of PIRCAM and Smoke Detector.
Smart Auto-pairing

## Slide 23
Repeater Setting/Status
Pairing
Click “Pairing” to boost the RF range of PIRCAM and Smoke detector.
Signal Strength Test
Click to test the Signal Strength between AX PRO Panel and Repeater
Find Me
Click “Find Me” button, and then LED indicator will blink for 30s, to help user find its location.

## Slide 24
04
Adding Relay.
Event linkage.
Relay
Configuration
Notes: 分类页

## Slide 25
Wall Switch
Relay Module
Smart Plug
Air Condition
Central Heating
Lamp
Electric Lock
Garage Door
Sounder
Air Fans
Water Heater
Humidifier
1-ch low current output(0~36VDC, 5A)
1-ch high current output(90~240VAC, 13A)
1-ch high current output(100~240VAC, 10A)
AX PRO Home Automation

## Slide 26
Relay configuration
Linked Area
Linked with a specific Area.
Original Status
Select “Normal Closed” or “Normal Opened” for output device.
Scenario Setting
Select Linkage Solution among “by Alarm” , “by Operation”, “by Fault”, “by Schedule”, and “Manual”.
Tamper Input
Enable this features if it’s in need to detect Tamper Alarm of output device.
Polling Rate
Set heartbeat time.

## Slide 27
05
Multiple methods for arming/disarming
“Arm with fault” features
Arm/Disarm
Operation
Notes: 分类页

## Slide 28
(Optional) Enable/Disable “Arm with fault”
“System” > “System Options”
Enable “Arm With Fault”
And select “CheckList”

## Slide 29
User configuration – Permission setting
Click “User Management”
Click Name Tag
Press the button
Set User Permission for user

## Slide 30
Keypad Operation
Notes:
When “Arm With Fault” is enabled. Panel will begin to check all the items you choose in “Checklist” in arming process, and the Fault LED will blink when they system detects any fault, you can stop the arming manually, or you can press Arm Button again to arm.
When “Arm With Fault” is disabled.
(But the system will not be compliant with the European EN50131-1 standard)
When you arm the system, the panel will be armed successfully no matter the system have fault or not.

## Slide 31
Keyfob Operation
Notes:
When “Arm With Fault” is enabled. Panel will begin to check all the items you choose in “Checklist” in arming process, and the Orange LED will blink when they system detects any fault, you can stop the arming manually, or you can press Arm Button again to arm.

## Slide 32
06
SMS / Voice Call
Video Verification
System
Operation
Notes: 分类页

## Slide 33
Press ‘>’ to add phone numbers
Press to continue
Add and configure
Add and configure
SMS / Voice Call Setting

## Slide 34
SMS / Voice Call Features
Notification SMS
Voice Call

## Slide 35
Video Verification
1.Adding IP Camera
Press ‘>’ to add camera
Press to add
Input parameters and save
Refresh and finish

## Slide 36
Video Verification
1.Zone Linkage
Select one detector you want to link
Press to configure
Press ‘>’ to link
Select one camera and finish

## Slide 37
Video Verification
Feature demonstration

## Slide 38
THANK YOU
International Product and Solution Center
Notes: 封底
产品图可更换，配图无需更换